## Slide 1
JITX · JUMPSTART KIT #1 · PART 2
Four component families,
no parts database
Yageo RC_L · Panasonic ERJ · Vishay CRCW · Samsung CL — straight from their datasheets
Drive jitx-component-modeler to build parameterized families where the class is the data — then ask for any part in the catalog and get an orderable MPN back.
Notes: Part 2 of JS1 — the first half of the component-handling pair. Datasheet tables become code here; Part 3 scales the idea to a 1,369-ball FPGA pin file.

## Slide 2
WHY THIS TASK
Model the family, not the part
Part 2 teaches: datasheet tables become code. One class stands in for a manufacturer's whole catalog family — sizes, tolerances, power ratings, packaging — transcribed once from the datasheet.
No parts database, no network. Ask for 49.9 kΩ ±1 % in 0402 and the class derives the dimensions, land pattern, ratings and the exact orderable MPN — entirely offline.
Fail fast, name the options. An invalid combination raises a ValueError that lists what the family actually offers — the datasheet's constraints, enforced at construction.
Abstraction earns its keep. Family 1 is built self-contained; shared helpers are extracted only when Family 2 proves the pattern repeats. Value encoders never merge — three vendors, three schemes.
2 / 6
Notes: The anti-premature-abstraction beat is deliberate teaching content, not a style preference.

## Slide 3
THE PATTERN
A shared core, a thin layer per vendor
SHARED CORE
chip_smt.py
• ChipDims — Toleranced package dimensions
• chip-size land-pattern generator
• two-pin insert (series drop-in)
• E-series value check
• carry-correct significant rounding
1
Yageo RC_L
RKM code → 100K
MPN RC0402JR-07100KL
2
Panasonic ERJ
EIA 3-digit → 103
MPN ERJ3GEYJ102V
3
Vishay CRCW
fixed 4-char RKM → 10K0
adds a TCR axis
4
Samsung CL (MLCC)
3-char pF code → 104
adds dielectric + voltage axes
Shared: geometry, insertion, validation helpers. Never shared: the vendor's value encoding and part-number grammar.
3 / 6
Notes: Three resistor vendors, three encoders — the lesson is where the abstraction boundary sits, not the encoders themselves.

## Slide 4
THE PIPELINE
What you build
Family 1 · Yageo RC_L, self-contained — eleven chip sizes, tolerance and packaging axes, RKM value codes. No helpers yet — nothing has repeated.
Family 2 · Panasonic ERJ, extract the core — the second family proves what's shared; chip_smt.py is born and Family 1 is refactored onto it.
Family 3 · Vishay CRCW — adds the TCR axis, and takes the generator's standard EIA dimensions — asserted per size against the datasheet's own table.
Family 4 · Samsung CL, the capacitor — the pattern generalizes across component type — dielectric and voltage axes, capacitor symbol, same shared core.
Proof by part number — RC0402JR-07100KL · ERJ3GEYJ102V · CRCW0603562RFKEA · CL10B104KB8NNNC — each encodes to the vendor's own catalog grammar.
4 / 6
Notes: Order matters — extraction happens at Family 2, and the shared module is renamed chip_resistor → chip_smt when the capacitor proves it was never resistor-specific.

## Slide 5
HOW WE KNOW IT'S RIGHT
Verification is the key
Datasheet spot-checks. Dimensions, ratings and codes are hand-read from the four datasheets and asserted in tests — per family, before it counts as done.
MPN cross-checks. Generated part numbers match the vendor's catalog listings character for character.
E-series discipline. Requested values validate against the tolerance's E-series grid, with carry-correct rounding before encoding.
Gates at every step. pyright → pytest → jitx build for every family, and jitx-code-review before the final commit.
The combined design. All four families instantiate together in one design that builds successfully — the showcase the closing prompt answers from.
5 / 6
Notes: A family is not done until it passes its tests and jitx build — same spine as Parts 1 and 3.

## Slide 6
WHERE TO START
Run it
The runbook: jumpstart-kits/js1-stackup-components/part2-parametric-passives/ — paste JS1_Part2_Parametric-Passives_Runbook.md into your agent and tell it to follow the file. Two [HUMAN] gates stop for you.
The ground truth: four manufacturer datasheets, fetched by URL during the run into a gitignored working folder — linked, never committed.
The reference solution: jitxexamples.jumpstart_kits.js1_stackup_components.parametric_passives — four families, the shared core, tests, and buildable designs.
CLOSE THE LOOP
“give me a 49.9 kΩ 0402 1 % Yageo and a 100 nF X7R 0603 50 V Samsung CL”
Two real, orderable parts — MPNs included — answered from code.
WHERE IT SITS Setup · JS0 → Stackup + Components · JS1 → Circuit Construction & Optimization · JS2
6 / 6
Notes: Each family lands verified and committed, so the session is pausable anywhere. Part 3 takes the same discipline to a vendor pin file.